## Slide 1
SEMANTIC NAVIGATION
Semantic navigation from live robot perception
A layered ROS 2 stack for building queryable semantic maps from camera, LiDAR, TF, and memory.
no mock detections
semantic memory
Nav2 integration
Camera
RGB detections
LiDAR
2D grounding
Memory
persistent map
Goal
semantic query
The system makes semantic navigation a runtime product of robot observation: what the robot sees, grounds, remembers, and relates becomes the map that downstream navigation uses.
semantic-nav architecture
01

## Slide 2
SEMANTIC NAVIGATION
End-to-end flowchart
The system converts pixels into semantic goals through explicit ROS 2 stages.
RGB image
camera topic
Detector
YOLO labels
Localizer
bearing + LDS range
Semantic memory
merge + promote
SemanticMapState
entities + relations
Query/Nav2
goal selection
Feedback loop
SLAM and TF continuously update the map frame. Semantic memory can refine entity validation when the occupancy grid catches up.
map / TF
semantic-nav architecture
02

## Slide 3
SEMANTIC NAVIGATION
Semantic map data model
The semantic nav dependency is structured around a hierarchy of map concepts.
SemanticMapState
SemanticEntity
object identity
pose + confidence
SemanticPlace
spatial grouping
region context
SemanticAnchor
stable reference
for approach goals
SemanticRelation
near / next_to
contains / supports
Entities are not isolated points; they are connected into places, anchors, and relations that queries can reason over.
semantic-nav architecture
03

## Slide 4
SEMANTIC NAVIGATION
Grounding real detections
Camera detections become usable only after robot-native spatial grounding.
Perception geometry
robot
detected object
occupancy_grid_validated
object point is inside the map and attached to obstacle evidence
occupancy_grid_pending
real LiDAR-grounded object, but local obstacle evidence is not ready yet
map_bounds_pending
object is real and grounded, but SLAM bounds have not expanded to it yet
semantic-nav architecture
04

## Slide 5
SEMANTIC NAVIGATION
Semantic memory state machine
Repeated real observations are merged before becoming navigation targets.
Observation
single grounded detection
merge
Candidate
merged over time
min observations
Landmark
persistent semantic entity
publish
SemanticMapState
published query snapshot
The memory node keeps provenance with each promoted landmark, so downstream navigation can distinguish validated entities from provisional ones.
semantic-nav architecture
05

## Slide 6
SEMANTIC NAVIGATION
Relationship mapping
The relationship layer turns objects into a navigable scene graph.
table
chair
person
room area
next_to
contains
near
Label mapping
Detector labels stay separate from semantic names. A detector label like bench can resolve to the user-facing concept table.
Vocabulary choice
Use robust relations like near and next_to instead of camera-relative left/right where viewpoint is unstable.
semantic-nav architecture
06

## Slide 7
SEMANTIC NAVIGATION
COLMAP enrichment for limited sensors
The visual reconstruction layer adds context without replacing robot safety grounding.
Nav safety layer
2D LiDAR + costmaps
Semantic layer
entities + relationships
Visual enrichment
COLMAP points / geometry context
enrich, do not replace
For 2D LiDAR robots, COLMAP helps recover visual geometry that the scan plane cannot see, while motion planning remains tied to the robot’s validated obstacle model.
semantic-nav architecture
07

## Slide 8
SEMANTIC NAVIGATION
Real robot integration
The system was prepared for a TurtleBot3-style ROS 2 deployment path.
LDS-02 bringup
real /scan source
USB camera path
real image stream
Nav2 lifecycle
active planner/controller/BT
Motion safety
unarmed until explicit test
Semantic route
memory publishes /semantic_map/state
Important real-world fix
When the detected table/bench was just outside the current SLAM map bounds, the old memory path dropped it. The new path keeps it as a real LiDAR-grounded provisional landmark until map validation catches up.
semantic-nav architecture
08

## Slide 9
SEMANTIC NAVIGATION
What changed here
The implementation is now organized around real full-stack runs, not demos or fake artifacts.
Removed mock artifacts
No fake COLMAP points, bootstrap people, or hardcoded semantic detections.
Routed semantic state
Persistent semantic memory now publishes the native SemanticMapState used by query.
Added provisional landmarks
Real LiDAR-grounded entities survive temporary occupancy-grid/map-bound gaps.
Validated packages
Coordinator and semantic-map packages build and test cleanly.
semantic-nav architecture
09

## Slide 10
SEMANTIC NAVIGATION
Result
A semantic navigation stack where meaning is built from live robot observations, not predefined scene knowledge.
The robot can move from “I see something” to “I understand what it is, where it is, how it relates to the scene, and whether it is safe to navigate toward.”
Built around: live perception, LiDAR grounding, persistent semantic memory, relationship mapping, COLMAP enrichment, and ROS 2/Nav2 integration.
semantic-nav architecture
10