## Slide 1
ROS 2 semantic navigation stack
01
SEMANTIC NAVIGATION
Semantic Navigation for ROS 2 Robots
A live perception stack that turns what the robot sees into a structured semantic map for navigation.
Core flow
Perceive
camera detections
Ground
2D LiDAR + TF
Remember
persistent entities
Navigate
queries to goals

## Slide 2
ROS 2 semantic navigation stack
02
SEMANTIC NAVIGATION
What We Built
The stack bridges low-level robot sensing and high-level language-style navigation requests.
Live perception
YOLO camera detections from the robot camera stream, with no mock detections or canned semantic objects.
Robot grounding
2D LiDAR, odometry, TF, and the occupancy grid provide the safety-relevant spatial frame.
Semantic navigation
Persistent semantic memory feeds a queryable map that can select targets and hand goals to Nav2.

## Slide 3
ROS 2 semantic navigation stack
03
SEMANTIC NAVIGATION
Runtime Architecture
Each stage has a narrow responsibility, so simulation and real robot deployments share the same data contracts.
Camera
image stream + detector labels
Localizer
pixel bearing + LiDAR range
Memory
stable object tracks
Semantic map
entities, places, relations
Query
user intent to target
Nav2
validated goal execution
The real robot path uses the same interfaces as simulation: detections are transformed into robot-relative objects, promoted into semantic memory, then published as SemanticMapState for query and navigation.

## Slide 4
ROS 2 semantic navigation stack
04
SEMANTIC NAVIGATION
Semantic Map Structure
The semantic map is a hierarchy, not a flat list of detections.
SemanticEntity
object identity, label mapping, confidence, provenance
SemanticPlace
clusters of entities that form navigable regions
SemanticAnchor
stable reference points for navigation and commands
SemanticRelation
spatial structure between entities and places
SemanticMapState
single queryable snapshot consumed by downstream nodes
Why this matters
The robot can reason over meaning and structure while still preserving sensor provenance. A target is not just a point; it is an object with identity, confidence, source, and relationships.

## Slide 5
ROS 2 semantic navigation stack
05
SEMANTIC NAVIGATION
Grounding, Memory, and Validation
The semantic system is built from live robot observations, then marked by validation state.
Detection
class + image box
LiDAR grounding
bearing + range
TF/map frame
robot pose context
Memory gate
merge + promote
Provenance states
occupancy_grid_validated
occupancy_grid_pending
map_bounds_pending
This lets the map use real LiDAR-grounded objects even when SLAM has not expanded far enough yet, without pretending they are fully grid-validated.

## Slide 6
ROS 2 semantic navigation stack
06
SEMANTIC NAVIGATION
Language-to-Map Reasoning
The query layer maps human intent onto the semantic map without coupling it to detector quirks.
Label mapping
Detector labels remain separate from semantic labels. For example, a model output such as bench can satisfy a user command for table when that better matches the environment.
detector_label: bench semantic_name: table
Relationship vocabulary
Spatial structure uses robust concepts like near and next to instead of brittle camera-relative left/right assumptions.
entity A next_to entity B place contains entity

## Slide 7
ROS 2 semantic navigation stack
07
SEMANTIC NAVIGATION
COLMAP as Visual Enrichment
Visual reconstruction is treated as enrichment, not as the safety authority.
Primary grounding
Robot-native sensors remain authoritative for safety and navigation. On the TurtleBot3 path, that means LDS-02 scan, odometry, TF, and Nav2 costmaps.
Visual enrichment
COLMAP-style reconstruction can add geometric context when LiDAR is sparse, 2D-only, or misses vertical structure.
Sim-to-real fit
The stack keeps the same interfaces whether enrichment is enabled or not, so robot deployments do not need to be restructured.
Design principle: use COLMAP to enrich spatial understanding, not to replace the robot validated obstacle model.

## Slide 8
ROS 2 semantic navigation stack
08
SEMANTIC NAVIGATION
Sim-to-Real Integration
The implementation was prepared and tested against a real TurtleBot3-style deployment path.
Integration work
ROS 2 Humble launch stack
TurtleBot3 Waffle configuration
LDS-02 LiDAR bringup
USB camera detector path
Nav2 lifecycle + plugin compatibility
Motion safety gate for real robot testing
Validation outcome
Real detections flowed through localization and memory. SemanticMapState is routed through persistent semantic memory. Provisional entities handle map-edge cases without introducing fake data.
Next: floor-space runs, calibration refinement, and longer mapping sessions.