## Slide 1
ROS 2 SEMANTIC NAVIGATION
Navigation over meaning, not just geometry.
A real robot stack that turns camera detections, 2D LiDAR, TF, and memory into a queryable semantic map.
live perception
semantic memory
Nav2 goals
Sense
camera + LDS-02
Ground
LiDAR + TF
Remember
persistent entities
Navigate
query to goal
semantic-nav / ROS 2
01

## Slide 2
SEMANTIC NAVIGATION
What the system does
It converts live robot observations into semantic objects with identity, confidence, provenance, and relationships, then exposes that structure to navigation.
No fake data
The real robot path removes mock detections and bootstrap points. Semantic state comes from camera perception and robot-grounded memory.
Structured memory
Objects are merged over time, promoted after repeated observations, and published as SemanticMapState.
Navigation-ready
Queries resolve to semantic targets and feed goal generation while Nav2 keeps motion bounded by the robot costmaps.
semantic-nav / ROS 2
02

## Slide 3
SEMANTIC NAVIGATION
Runtime architecture
Camera
RGB stream
Detector
YOLO labels + boxes
Localizer
bearing + scan range
Memory
stable tracks
SemanticMapState
entities / places / relations
Query + Nav2
target to goal
Each module owns one conversion: pixels to detections, detections to 2D grounded points, points to persistent entities, entities to navigable intent.
Design constraint: the same message contracts work in simulation and on the real TurtleBot3 deployment path.
semantic-nav / ROS 2
03

## Slide 4
SEMANTIC NAVIGATION
Semantic hierarchy
The semantic map is not a flat detection list. It is a layered structure the robot can query and reason over.
SemanticMapState
queryable snapshot
Relations
near, next_to, contains
Places + Anchors
regions and stable references
Entities
objects with labels, pose, confidence
Observations
camera detections grounded by robot sensors
Why it matters
The map preserves meaning and source quality. A target is an object with provenance, not just a coordinate.
semantic-nav / ROS 2
04

## Slide 5
SEMANTIC NAVIGATION
Grounding and validation
Camera-only detections are not enough. The stack grounds them in the robot frame before they can become navigation targets.
1. Visual detection
class + image-space box
2. LiDAR association
bearing to scan range
3. TF transform
base_link into map
4. Memory promotion
repeated observations become entities
Provenance-aware output
occupancy_grid_validated
occupancy_grid_pending
map_bounds_pending
semantic-nav / ROS 2
05

## Slide 6
SEMANTIC NAVIGATION
Language-to-map reasoning
Label mapping
Detector labels and human-facing semantic names are separate. A detector output like bench can still satisfy “go to the table” when that is the correct task-level concept.
Relationship mapping
The relation layer favors stable spatial vocabulary such as near and next_to, avoiding brittle camera-relative left/right assumptions.
command: “go to the table” -> semantic_name: table -> detector_label: bench -> selected entity pose
semantic-nav / ROS 2
06

## Slide 7
SEMANTIC NAVIGATION
COLMAP enrichment
For 2D LiDAR robots, visual reconstruction is useful context, but it should not replace robot-native safety grounding.
Safety source
LDS-02 scan, odom, TF, and Nav2 costmaps stay authoritative.
Visual context
COLMAP can add geometry where 2D LiDAR lacks vertical structure.
Enrichment layer
Semantic entities can be refined without changing robot interfaces.
Principle: enrich semantics with reconstruction; keep navigation safety tied to robot capabilities.
semantic-nav / ROS 2
07

## Slide 8
SEMANTIC NAVIGATION
Sim-to-real deployment
Robot target
TurtleBot3 Waffle-style ROS 2 Humble stack with LDS-02 LiDAR and USB camera perception.
Launch discipline
One real stack launch path, no fake detections, no bootstrap semantic objects, and motion initially gated for safety.
Validated flow
Camera detection -> localizer -> semantic memory -> SemanticMapState -> query/Nav2 integration.
Key fix from real testing: semantic landmarks can remain provisional when SLAM bounds lag behind LiDAR-grounded observations.
semantic-nav / ROS 2
08

## Slide 9
SEMANTIC NAVIGATION
What changed in this implementation
Clean real stack
Removed mock artifacts and routed semantic state through persistent memory.
ROS 2 compatibility
Fixed launch/config details for Humble, Nav2 lifecycle, and LDS-02 bringup.
SemanticMapState
Published persistent memory as the native semantic map consumed by query.
Provisional landmarks
Allowed real LiDAR-grounded entities to survive temporary map-edge conditions.
semantic-nav / ROS 2
09

## Slide 10
TAKEAWAY
The robot builds a semantic operating model from live perception.
Not a scripted map. Not fake detections. A layered, provenance-aware semantic map tied to the robot’s actual sensing and navigation stack.
objects
places
relations
goals
Next steps
Longer floor runs
Camera calibration
Richer relation vocabulary
COLMAP enrichment jobs
Query-driven exploration
semantic-nav / ROS 2
10